## Slide 1: Access Landsat-Based Evapotranspiration
15 November, 2022
Notes: National Aeronautics and Space Administration

## Slide 2: Objectives
By the end of this exercise, you will be able to subset and download evapotranspiration (ET) data over the Sao Francisco Verdadeiro (SFV) watershed using a Goggle Google Earth portal and import to QGIS
Requirements
QGIS installed on your computer
  https://arset.gsfc.nasa.gov/sites/default/files/water/drought/Introduction%20to%20QGIS.pdf
A shapefile for the Sao Francisco Verdadeiro watershed saved on your computer
  http://arset.gsfc.nasa.gov/

## Slide 3: Outline
Part 1: Select Landsat Images and Calculate METRIC ET
Part 2: QGIS analysis of the ET data for January & February 2016 and 2017

## Slide 4: Part 1: Select Landsat Images and Calculate METRIC ET

## Slide 5: Select Landsat Images and Calculate METRIC ET
Go to http://eeflux-level1.appspot.com/
On the EEFlux page you will see the following options:
  Instruction: provides information about the ET data and directions on how to use the EEFlux website
  FAQ: provides frequently asked questions
  Date Information: allows for date range selection
  Location Information: allows spatial selection by moving the orange marker on the world map. In the window the latitude and longitude values appear in decimal degrees as you move the marker.
  Search for Images: starts the search for images for the selected date range and spatial location

## Slide 6: Select Landsat Images and Calculate METRIC ET
Enter the following options:
  Date Information: Using the calendar, select 1 to 29 February 2016.
  Location: Drag the marker on the map to the latitude and longitude close to -24.47° and -54.01°
  Click on Search for Images. You will get a list of images with dates and percent cloud cover of the image

## Slide 7: Select Landsat Images and Calculate METRIC ET
In filenames LE7 is Landsat ETM+ (Landsat 7) and LC8 is OLI/TIRS combined from Landsat 8
In the image on the right: LC82240772016032LGN01
  224 and 077 are path and row of the image
  2016 is the year
  032 is the Julian Day
  the last five digits are for the ground station ID

## Slide 8: Select Landsat Images and Calculate METRIC ET
Click on the first image and you will see the Landsat image displayed on the map, along with a list of parameters derived from the image
Note the list of parameters available for this image:
  The reference ET for Alfalfa (ETr) and grass (ETo) surfaces are available
  ETrF is the ratio of actual ET (ETc) to ETr
  EToF is the ratio of ETc and ETo

## Slide 9: Select Landsat Images and Calculate METRIC ET
Examine each image in the list one by one and write down the cloud cover for each
  Note: the browser back arrow may not work. Click on the date and image window to go to the next image
Select the images one by one and click on Actual ET (Default)
  You will get the ET map on the right
  Look at the color bar on the left below the parameter list. Zoom in on the ET map to examine it closely.

## Slide 10: Select Landsat Images and Calculate METRIC ET
Download and save ET as a GeoTIFF file by clicking on the down arrow next to the Actual ET. You will get the files in .zip format. Unzip the files to get the ET data in GeoTIFF format.
Repeat the above steps for 1 to 28 February 2017 and save a GeoTIFF file for each day.

## Slide 11: Questions
Visually compare the ET maps for Landsat 7 images to that from Landsat 8 and comment on the difference you see in the quality of the data.
What is the unit of ET?
Compare the ET for images with different cloud cover. What happens when an image has large (>50%) cloud cover?

## Slide 12: Part 2: QGIS Analysis of ET Data for February 2016 & 2017

## Slide 13: QGIS Analysis of ET Data for February 2016 & 2017
Open QGIS and start a new project
From the top menu bar, click on Web, select Open Layer Plugin and select a background map
Click on the menu on the left bar and click Add Vector to add the SFW shapefile: sfv_4326.shp

## Slide 14: QGIS Analysis of ET Data for February 2016 & 2017
Make the shapefile layer transparent with only the boundary outlined on the map
  Right click on the layer file and go to Properties > Style
  Click on the down arrow in the Fill window and select Transparent fill
  Click on the down arrow in the Outline window and choose a color of the shapefile boundary (The example uses black)
  Choose outline width to be 2.0
  Click Apply and OK to get the result in the QGIS window

## Slide 15: QGIS Analysis of ET Data for February 2016 & 2017
Next click on the Add Raster function on the left
  Navigate to your saved ET files and click on Open to add the Landsat 8 data file: LC82240772016048LGN01_ETa.ETr.tif for February 17, 2016 and LC82240772017050LGN00_ETa.ETr.tif for February 19, 2017
  You will see the GeoTIFF images appear in grayscale

## Slide 16: QGIS Analysis of ET Data for February 2016 & 2017
Now clip the interpolated ET layers to the SFW shapefile
  On the top bar go to Raster > Extraction > Clipper to open the Clipper options window
  In the Input File (raster) window select: LC82240772016048LGN01_ETa.ETr.tif.
  In the Output file window, select the output folder and enter the file name (Suggestion: ET17Feb2016_Clipped)
  Check the Mask Layer and in the Mask Layer window select the shapefile named sfv_4326
  Click OK on at the bottom right
  You should see the data clipped by the shapefile boundary

## Slide 17: QGIS Analysis of ET Data for February 2016 & 2017
Repeat Step 6 for LC82240772017050LGN00_ETa.ETr.tif
  Suggestion: save the clipped file as ET19Feb2017_Clipped
  You can also remove the original ‘unclipped’ ET layers form the QGIS if you choose

## Slide 18: QGIS Analysis of ET Data for February 2016 & 2017
Right click on the clipped raster layers one at a time and follow the steps to get colored ET maps:
  Go to Properties > Style
  Select the Render Type as Singleband Pseudocolor
  Next to Color, make sure the color palette is Brown-Green by selecting (BrBG)
  Select Min value to be 0 mm/day and Max value to be 6 mm/day
  Below the color display, change the Mode to Equal Interval and Classes to 7. Click Classify, then click Apply
  Click OK to close the Change Color box

## Slide 19: QGIS Analysis of ET Data for February 2016 & 2017
Make the clipped ET layers transparent to see the map underneath
  Right click on the layer file and go to Properties > Transparency
  Set the Transparency level to 50%
  Under No data value set Additional no data value to 0
  Click Apply and then OK

## Slide 20: Questions
Which days show larger ET?
Which image has more cloud cover? Do you think the cloud cover has impact on the ET data?
Which factors decide what the ET values for any location or time will be?
What are the challenges with using Landsat ET for water budget analysis?