## Slide 1
Water quality from space
Daniel Andrade Maciel

## Slide 2
Pre-workshop preparations
Instructions for Google Earth Engine registration:
  If you are not registered yet, you can join GEE: https://earthengine.google.com/new_signup/
  Please, try to register before our workshop! It could take some days to Google approve your account.
Instructions for AQUASAT data download:
  This data could be freely obtained from https://figshare.com/articles/dataset/AquaSat/8139383 Please, download it and save to your computer before the workshop.

## Slide 3
Sensoriamento Remoto da cor da água
26 - 30 de Julho
Billings Reservoir, Brazil
Patos Lagoon, Rio Grande do Sul, Brasil

## Slide 4
Sensoriamento Remoto da cor da água
26 - 30 de Julho
Maracaibo Lake, Venezuela
Amazon River, Brasil
Santarém

## Slide 5
Chl-a, TSS, aCDOM, Secchi, Kd, PC
CDOM
Total particulate
phy
Particulado total
(TSM)
CDOM

## Slide 7
Algorithms
Empirical
Single Band
Semi-Analytical
Radiative transfer theory simplifications
Analytical
Radiative Transfer Theory
Machine Learning
Neural Networks
Band Ratio

## Slide 8
Reflectance (Red channel)
Sediment Concentraiton
Regression model
Y = ax + B
Empirical Algorithms
Single Bands
This is a very good fit!!
Does not happen in real life

## Slide 9
How to develop an empirical remote sensing algorithm for water quality?
Collect water quality data and (ideally) remote sensing in-situ data
Try to collect these data close to satellite overpass
Create a database that relates in-situ water quality and remote sensing data
Obtain satellite data close to in-situ measured points
Develop an algorithm and validate it
Apply to satellite data!!

## Slide 11
How to develop an empirical remote sensing algorithm for water quality?
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 12
How to develop an empirical remote sensing algorithm for water quality?
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 13
How to develop an empirical remote sensing algorithm for water quality?
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 14
How to develop an empirical remote sensing algorithm for water quality?
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 15
How to develop an empirical remote sensing algorithm for water quality?
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 16
How to develop an empirical remote sensing algorithm for water quality?
Reflectance (Red channel)
Sediment Concentraiton
Regression model
Y = ax + B
blue | green | red | nir | secchi | tss | lat | long
0.007 | 0.008 | 0.007 | 0.012 | 5.6 | 3.83 | 45.5 | -67.8
0.006 | 0.007 | 0.004 | 0.008 | 9.1 | 4.1 | 45.5 | -67.8
0.017 | 0.016 | 0.012 | 0.020 | 5.6 | 3.3 | 45.5 | -67.8
0.009 | 0.009 | 0.007 | 0.012 | 3.1 | 3.7 | 45.6 | -67.6
0.005 | 0.004 | 0.003 | 0.007 | 6.7 | 2.8 | 45.6 | -67.6
0.012 | 0.013 | 0.012 | 0.021 | 8.7 | 4 | 45.6 | -67.6
0.006 | 0.006 | 0.004 | 0.008 | 0.14 | 3.5 | 45.6 | -67.6
0.005 | 0.005 | 0.003 | 0.005 | 1.3 | 5.5 | 45.6 | -67.6
0.008 | 0.009 | 0.008 | 0.011 | 5.6 | 6.15 | 45.6 | -67.6

## Slide 17
How to develop an empirical remote sensing algorithm for water quality?
Reflectance (Red channel)
Sediment Concentraiton
Regression model
Y = ax + B
Validation Metrics:
Error: 30%
R2: 0.92
BIAS: 10%

## Slide 18
Hands on!!
Dataset used
Our Final results

## Slide 19
More resources
  International Ocean Colour Coordinating Group (IOCCG):
    In situ calibration/validation protocols [access here]​
    Satellite missions
    Task Force on Remote Sensing of Marine Litter and Debris
    Earth Observations in Support of Global Water Quality Monitoring – Report
  Educational Materials​
    Optics webbook​
  ​GEO AquaWatch
  Copernicus
    Open Access Hub
    Global Land Service
  United States Geological Survey
    Earth Explorer​
  MISC Lab
    Ocean Optics Classes
  European Space Agency
    Climate Change Initiative: Lakes​
  Sentinel Application Platform (SNAP)
    Earth Online
    SNAP Toolboxes​
    SNAP Tutorials
  NASA Resources:
    Applied Remote Sensing Training Program (ARSET)
    Data visualization and analysis webtool
    In situ ocean color network
    Processing software
    Upcoming ocean color mission
  LabISA/INPE resources
    Website
    Introduction to Remote Sensing of Aquatic systems (Portuguese)