## Slide 1: Climate Risk-Informed Decision Analysis (CRIDA): Integrating Climate Resilience within Existing Water Resources Planning, Design and Operations
William S. (Will) Logan, PhD
Director, International Center for Integrated Water Resources Management (ICIWaRM)
Institute for Water Resources, USACE
Collaborators include UNESCO, Deltares, Alliance for Global Water Adaptation (AGWA), University of Massachusetts, University of Cincinnati, (Rijkswaterstaat, World Bank)

## Slide 2: Why CRIDA?
There’s been a lot of thinking about Climate Adaptation and about Water Resources Management
Many seem to think that we need to treat our adaptation challenges as a climate science problem.
I.e., climate science can come in and rescue us and provide us with resilient systems.
But water resources management is still a water problem. We need to build on what we know, not take an entirely new direction.

## Slide 3: Climate models, designed and run by climatologists, project future climate
Meteo-France model, from IPCC

## Slide 4: But they often disagree with each other
The Meteo-France and Australian models (IPCC)

## Slide 5: … and we don’t have just two models… We have lots of models…

## Slide 6: … and future climates depend on future climate policies and socio-economic trends…

## Slide 7: The Frustration with Downscaling Global Climate Models and the Origin of CRIDA
World Bank 2011
“We hire a contractor to help assess climate change impacts. On completion an inch thick report is produced to state that the future is uncertain” Luis Garcia, World Bank
Wilby and Dessai 2010

## Slide 8: Prediction Variation among 9 GCMs for Philadelphia, USA by Storm Size and Season
Source: Mark Maimone, CDM-Smith, 2020

## Slide 9
• Access to capital
• Subsidies of green or gray technologies
* Interest group mobilization
• Carbon lock-in
• Environmental justice/ moral acceptability
• Public opinion
• Confidence in political institutions
• Trade and investment policies
• State intervention in markets
• Cost of deploying capital. • Etc…etc…etc…
Some people think we just need more complex climate models…REALLY?

## Slide 10: We have spent a lot of time trying to optimize water plans, rather than making them robust to changing conditions

## Slide 11
What keeps a planner awake at night?
1a. Perform Vulnerability Assessments with Stakeholders
Vulnerability domain
2. Stress Test
3. Determine plausibility and consequence
Forecasting - Optimization (top-down)
Scenario Planning – Risk Informed (bottom-up)
Critical climate and other urbanization stressors
GCMs
Tested vulnerability domain
1. Downscale multiple model projections
2. Hope the GCMs are correct.
3. Generate a few water supply series.
4. Find whether system is vulnerable for these series
Unhelpful GCM-based Planning vs. Bottom-Up Scenario Planning with Stakeholders
Planning Scenarios
Notes: 11

## Slide 12: CRIDA Steps (orange) Parallel Typical Water Resources Planning Steps (blue)

## Slide 13: Sometimes system failure is not all about climate change
Alexis Dufour, SFPUC Water Enterprise
Notes: Note the huge number of potential uncertainties. Climate is one of 13.

## Slide 14: Step 1: Structuring a Collaborative Process for Vulnerability Assessment
Water resources system model
External drivers
Performance metrics
Critical thresholds

## Slide 15: Shared Vision Planning/ Stakeholder Engagement
Shared Vision Planning (SVP) is a collaborative approach to formulating water management solutions that combines three disparate practices:
  Traditional water resources planning
  Structured public participation &
  Collaborative computer modeling
Notes: Stacy

## Slide 16: Stakeholders know lots about your system, and know what system failure is all about

## Slide 17: Key Elements of a Water Resources Systems Model

## Slide 19: Many interest groups, which may have lots of suggestions for performance indicators
1. Recreation Boating & Tourism
2. Commercial Navigation
3. Environment
4. Municipal and Industrial Water Uses
5. Hydropower
6. Coastal
Example from the Binational (US-Canada) Great Lakes-St. Lawrence Seaway system

## Slide 20: Some examples of Great Lakes Performance Indicators
Economic
  Transportation costs (Navigation)
  Infrastructure Investment Costs (Municipal/Industrial)
  Water Quality Investments (Municipal/Industrial)
  Willingness to Pay (Recreation)
  Cost of foregone peaking opportunities (Hydropower)
Environmental Quality
  32 key performance indicators (too many!)
Social well-being
  Beach access (Coastal)
  Four indicators for Floods (Coastal)

## Slide 21: Step 2: Implementing a Bottom-up Vulnerability Assessment
Input from Step 1
• Water resources system model
• External drivers
• Performance metrics
• Critical thresholds
Output from Step 2
• Stress test results showing the limits of performance
• An assessment of the plausibility that future stressors will lead to unacceptable performance
• An assessment of analytical uncertainty and how it affects the choice of options
• A measure of level of concern based on the assessment of plausibility and analytical uncertainty

## Slide 22
Vulnerability Assessment – Stress Test
Plausibility of “Failure”
(In this case, <220 hm3 flow into the reservoir, Limari Basin, Chile)
Source: Koen Verbist

## Slide 23
(a) High scatter in data and (b) ~75% of simulations suggesting system failure puts us in Quadrants III or IV
Notes: Level of concern:• Does credible evidence suggest a threshold will be crossed leading to unacceptable
performance?
• Is the confidence level of the analysis sufficient to make a risk-informed decision?
In Limari, concern was estimated with questionnaires. In San Francisco, with an expert panel

## Slide 24: Step 3: Formulating Alternative Plans
Input from Step 2
• Stress test results showing the limits of performance
• An assessment of the plausibility that future stressors will lead to unacceptable performance
• An assessment of analytical uncertainty and how it affects the choice of options
• A measure of Level of Concern, based on the assessment of plausibility and analytical uncertainty
Output from Step 3
• Robust and flexible plans, based on
- reducing relative risks and
- comparing alternative solution comprehensiveness, effectiveness, and stakeholder acceptability

## Slide 25
Developing an “Adaptation Pathways” Map

## Slide 26
Developing Adaptation Pathways “Tipping Points”

## Slide 27
Adaptation Pathways as a metro system
Some paths are shorter
But maybe the trains break down earlier
But in some cases if I know that, I can detour around a problem.
Or maybe I should take a taxi, but it’s expensive.
Or walk, which is free, low-risk but high-effort.

## Slide 28: Developing Adaptation Pathways: Tipping Points

## Slide 29: Identify Adaptation Pathways “Transfer Points”

## Slide 30: Simplifying the Adaptation Pathways Map

## Slide 31: Step 4: Comparing and Recommending Plans
Input from Step 3
• Robust and flexible plans based on risk reduction, comprehensiveness and completeness, effectiveness in meeting planning objectives, and stakeholder acceptability
Output from Step 4
• Comparison of plans against a baseline measure of performance
• Comparison of plans across different future scenarios
• Recommended plan(s) to the decision maker

## Slide 32: Incremental Cost Analysis

## Slide 33
What keeps a planner awake at night?
1a. Perform Vulnerability Assessments with Stakeholders
Vulnerability domain
2. Stress Test
3. Determine plausibility and consequence
Forecasting - Optimization (top-down)
Scenario Planning – Risk Informed (bottom-up)
Critical climate and other urbanization stressors
GCMs
Tested vulnerability domain
1. Downscale multiple model projections
2. Hope the GCMs are correct.
3. Generate a few water supply series.
4. Find whether system is vulnerable for these series
Unhelpful GCM-based Planning vs. Bottom-Up Scenario Planning with Stakeholders
Planning Scenarios
Notes: 33

## Slide 34: Who is using CRIDA?

## Slide 35: World Bank “Decision Tree Framework” and CRIDA

## Slide 36
Capacity building as a tool for upscaling CRIDA
A CRIDA online course was developed in 2020, reaching already 2840 learners from 114 countries.
A Spanish and English version of the CRIDA course was launched in March 2022 and a French and Arabic (and repeat of English) in November 2022.
https://openlearning.unesco.org/

## Slide 37: Thank you
https://iwaponline.com/wp/issue/23/S1